## Slide 1
STABILIZE
Non-linear control law for mom. wheel + 2-axis magnetorquers
DETUMBLE
B-Dot control law with 3-axis magnetorquers
SLEW
Non-linear control law for mom. wheel + 2-axis magnetorquers
norm() > TUMBLE_LIM for DEBOUNCE_TIME
norm() > TUMBLE_LIM for DEBOUNCE_TIME
norm() < TUMBLE_LIM for DEBOUNCE_TIME
all( err_ang < LARGE_ANGLE_LIM ) for DEBOUNCE_TIME
any( err_ang > LARGE_ANGLE_LIM )
angular velocity, princ. axes
maximum magnitude off-diagonal elements of control error DCM
TUMBLE_LIMIT = spin rate at which spacecraft switches to DETUMBLE mode
LARGE_ANGLE_LIM = angle in radians above which the non-linear control law should be used (SLEW mode)
DEBOUNCE_TIME = time in seconds, acts to prevent high-frequency state transitioning